Re-fitting the DoAr21 spectrum near the Si XIV line

Using Marc’s remade rmfs and garfs

16 Oct 2006

Powerlaw index = 2; norm free

C-stat

On (ignore: 0.0-6.00, 6.14-6.22, 6.35-**) N=52 bins

MEG -1

norm=3.51e-3

Cstat=32.09

goodness=1%

MEG +1

norm=3.92e-3

Cstat=55.22

goodness=50%

N=106 bins over same wavelength range in the HEG

HEG -1

norm=3.39e-3

Cstat=112.59

goodness=23%

HEG +1

norm=3.96e-3

Cstat=99.32

goodness=7%

These values are now in pretty good seeming agreement.  Are they formally consistent with each other?

3.65e-3 : 4.25e-3 is the 68% confidence range (DeltaC=1) for the HEG+1 data

3.13e-3 : 3.66e-3 for HEG-1

3.30e-3 : 3.73e-3 for MEG-1

3.73e-3 : 4.10e-3 for MEG+1

2. FITTING LGAUSS + POW TO THE LINE AND NEARBY CONTINUUM

include 6.12:6.26 (so, less continuum) for the MEG

use the powerlaw continuum fits found above

first, fit one arm at a time

flux-weighted wavelength 6.1822

MEG -1

---------------------------------------------------------------------------

Model:  lgauss<1> + powerlaw<2>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   lgauss     waveleng A          6.18101     +/-  0.766898

2    2    1   lgauss     sigma    mA         3.31913     +/-   3.74697

3    3    1   lgauss     norm               2.133308E-05 +/-  0.614124E-05

4    4    2   powerlaw   PhoIndex            2.00000     frozen

5    5    2   powerlaw   norm               3.510000E-03 frozen

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      19.82894     using    27 PHA bins.

Akaike Information Criterion =      129.9601

Bayesian Information Criterion =      140.3388

XSPEC>plot

XSPEC>goodness nosim 100

18.00% of realizations have a fit statistic <      19.83

MEG +1

---------------------------------------------------------------------------

Model:  lgauss<1> + powerlaw<2>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   lgauss     waveleng A          6.18300     +/-  0.681443

2    2    1   lgauss     sigma    mA         2.70485     +/-   3.70431

3    3    1   lgauss     norm               2.014430E-05 +/-  0.463579E-05

4    4    2   powerlaw   PhoIndex            2.00000     frozen

5    5    2   powerlaw   norm               3.920000E-03 frozen

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      17.99811     using    27 PHA bins.

XSPEC>goodness nosim 100

8.00% of realizations have a fit statistic <      18.00

Combined +1/-1 MEG fit:

---------------------------------------------------------------------------

Model:  lgauss<1> + powerlaw<2>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   lgauss     waveleng A          6.18223     +/-  0.445459

2    2    1   lgauss     sigma    mA         3.46990     +/-   2.48399

3    3    1   lgauss     norm               2.101552E-05 +/-  0.442108E-05

4    4    2   powerlaw   PhoIndex            2.00000     frozen

5    5    2   powerlaw   norm               3.615801E-03 +/-  0.361336E-03

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      38.57593     using    54 PHA bins.

XSPEC>goodness nosim 100

6.00% of realizations have a fit statistic <      38.58

For HEG fit [6.16:6.21] using the power-law continuum fits listed above

HEG -1

---------------------------------------------------------------------------

Model:  lgauss<1> + powerlaw<2>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   lgauss     waveleng A          6.18350     +/-  -1.00000

2    2    1   lgauss     sigma    mA        4.855193E-02 +/-  -1.00000

3    3    1   lgauss     norm               1.981350E-05 +/-  0.639536E-05

4    4    2   powerlaw   PhoIndex            2.00000     frozen

5    5    2   powerlaw   norm               3.390000E-03 frozen

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      9.514089     using    19 PHA bins.

Akaike Information Criterion =      70.95518

Bayesian Information Criterion =      77.94739

XSPEC>plot

XSPEC>goodness nosim 100

0.00% of realizations have a fit statistic <      9.514

HEG +1

---------------------------------------------------------------------------

Model:  lgauss<1> + powerlaw<2>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   lgauss     waveleng A          6.18310     +/-   224481.

2    2    1   lgauss     sigma    mA         4.03149     +/-   1.78121

3    3    1   lgauss     norm               1.928333E-05 +/-  0.749858E-05

4    4    2   powerlaw   PhoIndex            2.00000     frozen

5    5    2   powerlaw   norm               3.960000E-03 frozen

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      17.41483     using    19 PHA bins.

XSPEC>goodness nosim 100

38.00% of realizations have a fit statistic <      17.41

combined HEG:

---------------------------------------------------------------------------

Model:  lgauss<1> + powerlaw<2>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   lgauss     waveleng A          6.18300     +/-  -1.00000

2    2    1   lgauss     sigma    mA        0.534587     +/-  0.521688

3    3    1   lgauss     norm               1.765386E-05 +/-  0.469634E-05

4    4    2   powerlaw   PhoIndex            2.00000     frozen

5    5    2   powerlaw   norm               3.650000E-03 frozen

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      31.28625     using    38 PHA bins.

XSPEC>goodness nosim 100

11.00% of realizations have a fit statistic <      31.29

Finally, combined HEG + MEG, both -1 and +1

First, fit a continuum to the combined data:

---------------------------------------------------------------------------

Model:  powerlaw<1>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   powerlaw   PhoIndex            2.00000     frozen

2    2    1   powerlaw   norm               3.729019E-03 +/-  0.165993E-03

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      303.4495     using   316 PHA bins.

Akaike Information Criterion =      1125.339

Bayesian Information Criterion =      1130.315

XSPEC>plot

XSPEC>goodness nosim 100

2.00% of realizations have a fit statistic <      303.4

Now fit the line with this continuum level fixed

6.14:6.23

---------------------------------------------------------------------------

Model:  lgauss<1> + powerlaw<2>

Model Fit Model Component  Parameter  Unit     Value

par   par comp

1    1    1   lgauss     waveleng A          6.18314     +/-   3.92931

2    2    1   lgauss     sigma    mA         1.95399     +/-   1.22807

3    3    1   lgauss     norm               1.940000E-05 +/-   0.00000

4    4    2   powerlaw   PhoIndex            2.00000     frozen

5    5    2   powerlaw   norm               3.730000E-03 frozen

---------------------------------------------------------------------------

---------------------------------------------------------------------------

C-statistic =      105.5544     using   104 PHA bins.

XSPEC>goodness nosim 100

31.00% of realizations have a fit statistic <      105.6

68% confidence limits:

lambda: 6.18248 – 6.18461

sigma:  0.1 – 3.4 mA

norm: 1.79e-5 : 2.09e-5